This checklist will help the analyst identify the contributing factors that contributed to the error. [Remember, if two or more errors combined to cause the event, it is important to identify which factors relate to which error.] There are ten major categories of contributing factors in the checklist:

A. Information

B. Equipment, tools, and safety equipment

C. Aircraft design, configuration, and parts

D. The job or task

E. Technical knowledge and skills

F. Individual factors

G. Environment and facility

H. Organizational factors

I. Leadership and supervision

J. Communication There is also an eleventh category (K) “Other” that is to be used in case the contributing factor cannot be found in A through J. (usually not valid)

(a) Information

Information refers to the written or computerized source data that a maintenance technician needs to carry out a task or job. It includes workcards, maintenance manual procedures, service bulletins or engineering orders, maintenance tips, illustrated parts catalogs and other manufacturer supplied or internal resources.

Information does not include verbal instructions from supervisors, shift handover logs, etc., which are considered to be Communication on the Results Form

To determine that information was a contributing factor to the maintenance error, either the information itself must be problematical (e.g., hard to understand, not complete, conflicting), or the information should have been used but was not (e.g., it was not available, it was ignored).

If it is expected that the maintenance technician has this information memorized, then refer to the Technical Knowledge/Skills section.

Information examples to look for:

Not understandable

Unfamiliar words or acronyms

Unusual or non-standard format

Poor or insufficient illustrations

Not enough detail or missing steps

Poorly written procedures

Unavailable / Inaccessible

Procedure does not exist

Not located in correct or usual place

Not located near worksite

Incorrect

Missing pages or revisions

Does not match aircraft configuration

Transferred from source document incorrectly

Steps out of sequence

Not the most current revision

Procedure does not work

Too much / conflicting information

Similar procedures in different resources do not agree (e.g. MM v task card)

Too many references to other documents

Configurations shown in different resources do not agree

Update process is too long / complicated

Requested revisions have not been incorporated yet

Configurations changed by Service Bulletins or Engineering Orders have not been updated in applicable maintenance procedures

Document change requests are not submitted, lost, or incorrectly filled out

Incorrectly modified manufacturer's MM/SB

Intent of manufacturer's procedure is not met

Non-standard practices or steps are added

Format does not match rest of procedure or other procedures

Information not used

Not using technical documentation is potentially a violation. If the technician should have used the documentation, but did not, find out why (i.e., what the contributing factors were to not using the documentation).

Procedure available but the technician did not have enough time to get it

Technician thought that he did not need the procedure because he had done the task many times before

Other

Example - Operator cannot use digital information

(b) Equipment/Tools/Safety Equipment

Equipment, tools and safety equipment are the tools and materials necessary for the safe performance of a maintenance task. Equipment and tools refer to things such as nondestructive test equipment, work stands, calibrated torque wrenches, screwdrivers, test boxes, and special tools called out in maintenance procedures. Safety equipment includes both personal protective equipment, such as hard hats and safety harnesses, as well as collective safety devices, such as hazard barriers and safety railings.

Unsafe equipment and tools may cause a maintenance technician to become distracted from the task due to concern for personal safety. If equipment or tools are not available or are inaccessible, the maintenance technician may use other equipment or tools that are not fully suited for the job. Other factors that can contribute to error include miss-calibrated instruments, use of unreliable equipment, or equipment or tools with no instructions for use.

Equipment/Tools/Safety Equipment - Examples to look for:

Unsafe

Platform moves and is unstable

Brakes or safety devices inoperative

Non-skid material worn or missing

A lock-out mechanism is missing or faulty

Placards (warnings or cautions) are missing or faded

Sharp edges are exposed or personal protective devices are missing

Power sources are not labeled or protected

Unreliable

Intermittent or fluctuating readings on dials or indicators

Damaged or worn out

Expired use limits

History of defects

Layout of controls or displays

Easy to read wrong display or use wrong control

Awkward locations, hard to reach

Too small to read or control

Directional control of knobs or dials is not clear

Mis-calibrated

Tool out of calibration from the start of use

Wrong specifications used during calibration procedure

Unavailable

Is not owned or in stock

Not available for procurement

Inappropriate for the task

Standard hand tools used for leverage

Not capable of handling weights, forces, or pressures required for the task

Connections or grips not the right size

Cannot be used in intended environment

Not enough space to operate tool

Requires level surface where one is not available

No instructions

Instructional placards missing or faded

Directional markings missing

Tool usage instructions not available

Too complicated

Tool usage requires too many simultaneous movements and/or readings

Fault isolation or testing is too complex

Incorrectly labeled

Hand marked labeling or operating instructions are incorrect

Tool has incorrect scale readings

Not used

Equipment/tool/part is available but not used. Not using the correct equipment/tools/safety equipment is potentially a violation. If the technician did not use the correct equipment/tools/safety equipment, find out why (i.e., what the contributing factors to not using it).

Incorrectly used

Safety equipment not appropriate for the hazard

Personal protective equipment not properly worn

Other

System protection devices on tools/equipment not available

(c) Aircraft Design / Configuration / Parts

An aircraft should be designed/configured so that parts and systems are accessible for maintenance. The maintenance technician should be able to see and reach a part, should be able to remove it from a reach and strength standpoint, and should be able to easily replace the part in the correct orientation. When reviewing accessibility as a contributor to maintenance error, it must be seen as a real contributor to the error and not just as an inconvenience to the maintenance technician.

Configuration variability between models and aircraft can contribute to error when there are small differences between the configurations that require maintenance tasks to be carried out differently or require slightly different parts.

Parts refer to aircraft parts that are to be replaced. Incorrectly labeled parts can contribute to improper installation or repair. Parts that are unavailable can contribute to error by the maintenance technician who uses a substitute part.

Good part design also incorporates feedback that helps the maintenance technician know that something has been performed correctly. For example, an electrical connector that has a ratchet effect provides feedback to the maintenance technician when the installation is correct. If this ratchet effect is included in some connectors and not others, this could contribute to error.

If a maintenance technician goes from a ratchet connector to a non-ratchet connector, the technician may over tighten the second connector looking for the ratchet.

Aircraft Design / Configuration / Parts - examples to look for:

Complex

Fault isolation on the system or component is difficult

Installation of components is confusing, long, or error prone

Multiple similar connections exist on the system or component (electrical, hydraulic, pneumatic, etc.)

Installation tests for the component are extensive and confusing

Different sized fasteners can be installed in multiple locations

Inaccessible

Components or area to be maintained is surrounded by structure

No access doors exist in the maintenance area

Area lacks footing space or hand-holds

Small or odd-shaped area

Aircraft configuration variability

Similar parts on different models are installed differently

Aircraft modifications have changed installation or other maintenance procedures between aircraft

Parts unavailable

Part not owned or in stock

Not available for procurement

Parts incorrectly labeled

Hand marked labeling incorrect

Wrong part number on part

Easy to install incorrectly

Can be easily installed with wrong orientation No orientation indicators (e.g., arrow, colors) Connections identical in size, color or length

Other

If the correct part was available, but was not used, then this could be a violation.

If the technician did not use the correct part when it was available, find out why (i.e., what the contributing factors to not using it).

Components are too heavy for easy removal/installation

Lack of feedback provided by component or system

Direction of flow indicators do not exist

(d) Job/Task

A maintenance technician's job/task can logically be separated into a series of tasks. If the interviewer feels the task was a contributing factor, he should analyze the combination or sequence of tasks. The interviewer, when examining the task sequencing, should also determine whether written information was being used, what technical skills and knowledge were expected of the maintenance technician, and what communication took place.

Job / Task examples to look for:

Repetitive / monotonous

Similar steps are performed over and over (opening and closing circuit breakers during a long test)

The same task performed many times in multiple locations (removing seats)

Complex / confusing

Multiple other tasks are required during this task

Multiple steps required at the same time by different maintenance technicians

Long procedure with step sequences critical

System interacts with other systems during testing or fault isolation

Multiple electrical checks are required

Task requires exceptional mental or physical effort

New task or task change

New maintenance requirement or component

Revision to a procedure

Engineering modification to existing fleet

New aircraft model

Different from other similar tasks

Same procedure on different models is slightly different

Recent change to aircraft configuration has slightly changed task

Same job at different worksites is performed slightly different

Other

The workgroup performs the task differently than specified in the source data (or written information)

(e) Technical Knowledge / Skills

Technical skills (sometimes also referred to as abilities) refer to tasks or subtasks that maintenance technicians are expected to perform without having to refer to other information. Technical skills include such things as being able to lock wire, use a torque wrench, and remove common parts from an aircraft. For (lack of) technical skills to be a contributing factor to error, the technician must not have skill that was generally expected of him/her.

Technical knowledge refers to the understanding of a body of information that is applied directly to performing a task. Technical knowledge, in order to be a contributing factor to error, is knowledge that is supposed to be known (memorized) by the maintenance technician. Three broad categories of knowledge are required of a technician: airline process knowledge, aircraft systems knowledge, and maintenance task knowledge. These are discussed in more detail below.

Airline process knowledge refers to knowledge of the processes and practices of the airline or repair station in which the maintenance technician works. Examples include shift handover procedures, parts tagging requirements, and sign off requirements. While this knowledge is generally acquired through general maintenance operating procedures and on-the-job discussion with peers, it may also be acquired from other sources such as employee bulletins and special training.

Aircraft system knowledge refers to knowledge of the physical aircraft systems and equipment. Examples include location and function of hydraulic pumps and rework options for corroded or fatigued parts. While this knowledge is generally acquired from the aircraft design characteristics, training, maintenance manuals, and on-the-job discussion with peers, it may also be acquired from other sources such as trade journals and maintenance tips.

Maintenance task knowledge refers to the specific knowledge required to perform a unique task. Examples include the procedure for bleeding a hydraulic system and for measuring tire wear. While this knowledge is generally acquired through maintenance instructions or on-the-job discussions with peers, it may also be acquired from aircraft placards, design characteristics, or even other maintenance technicians when working as a team.

Technical Knowledge / Skills examples to look for:

Skills

Safety wiring

Rigging of controls

Using calibrated equipment

Carrying out a fault isolation task

Task knowledge

Slow task completion

Technician change of maintenance responsibilities

Task performed by maintenance technician for the first time

Task performed in wrong sequence

Task planning

Frequent work interruptions to get tools or parts

Failure to perform preparation tasks first

Too many tasks scheduled for limited time period

Task necessary for safety not performed first

Airline process knowledge

If the technician knows the correct airline process to follow, but does not do so, then this could be a violation. If the technician did not follow the process correctly, find out why (i.e., what the contributing factors to not following the airline process).

Failure to acquire parts on time

Technician new to airline or to type of work (from line to hangar, etc.)

Airline processes not documented or stressed in training

Aircraft system knowledge

Technician changes aircraft types or major systems

Fault isolation takes too much time or is incomplete

Other

Technician performance/skills not accurately tracked/measured

(f) Individual Factors

Individual factors vary from person to person and include body size/strength, health, and personal events and the way that a technician responds to things such as peer pressure, time constraints, and fatigue caused by the job itself.

Physical health includes the acuity of human senses as well as physical conditions and physical illnesses. Human senses, especially vision, hearing, and touch, play an important role in maintenance. Technicians are frequently required to perform tasks that are at or near the limits of their sensory capabilities. For example, some tasks require good vision and/or touch, such as visual inspection for cracks or finger inspection for burrs. Good hearing is also required in order to hear instructions or feedback before and during a maintenance task.

Physical conditions, such as headaches and chronic pain, also have been shown to relate to errors. Alcohol/drug use, as well as side effects of various prescription and over-the-counter medicines, can negatively affect the senses. Physical illness, such as having a cold or the flu, can also negatively affect the senses and the ability to concentrate. Illnesses can also lead to less energy, which can affect fatigue.

Fatigue has been defined by the U.S. Federal Aviation Administration (FAA) as a depletion of body energy reserves, leading to below-par performance. Fatigue may be emotional or physical in origin. Acute fatigue may be caused by emotional stress, depletion of physical energy, lack of sleep, lack of food, poor physical health, or over excitement. Fatigue may also be caused by the work situation itself. The time of the day, the length one has been working, and complex mental tasks or very physical tasks can cause fatigue.

A technician’s response to time constraints or time "pressure" is an individual factor. The need to finish a maintenance task so an aircraft can be released from the gate or to finish a heavy maintenance task so an aircraft can be put back into service often cause technicians to feel pressure to get their tasks done. Studies have linked too little time with increased error. There is a well-known speed/accuracy trade-off, in that the faster one tries to finish a task the more likely an error is to happen. This trade-off also holds for speed and safety.

A technician’s response to peer pressure can also influence their performance. For example, there may be peer pressure not to use maintenance manuals because it is seen as a sign of lack of technical knowledge. Peer pressure may also influence a technician's safety-related behavior.

Complacency is over-contentment with a situation that may lead to a failure to recognize cues that indicate a potential error. Body size and strength are two obvious factors that affect a maintenance technician's ability to perform a task. If someone is too small to reach a plug or if someone is unable to let down an LRU from an upper rack, this can contribute to error.

Individual Factors examples to look for:

Physical health

Sensory acuity (e.g. vision loss, hearing loss, touch)

Failure to wear corrective lenses

Failure to use hearing aids or ear plugs

Restricted field of vision due to protective eye equipment

Pre-existing disease

Personal injury

Chronic pain limiting range of movement

Nutritional factors (missed meals, poor diet)

Adverse affects of medication

Drug or alcohol use

Complaints of frequent muscle/soft tissue injury

Chronic joint pain in hands/arms/knees

Fatigue

Lack of sleep

Emotional stress (e.g. tension, anxiety, depression)

Judgment errors

Inadequate vigilance, attention span, alertness

Inability to concentrate

Slow reaction time

Significant increase in work hours or change in conditions

Excessive length of work day

Excessive time spent on one task

Chronic overloading

Task saturation (e.g., inspecting rows of rivets)

Time constraints

Constant fast-paced environment

Multiple tasks to be performed by one person in a limited time

Increase in workload without an increase in staff

Too much emphasis on schedule without proper planning

Perceived pressure to finish a task more quickly than needed in order to release the aircraft from the gate

Peer pressure

Unwillingness to use written information because it is seen as a lack of technical skills/knowledge

Lack of individual confidence

Not questioning other's processes

Not following safe operating procedures because others don't follow them

Complacency

Hazardous attitudes (invulnerability, arrogance, over-confidence)

Task repetition leads to loss of mental sharpness or efficiency

Body size/strength

Abnormal reach, unusual fit, or unusual strength required for the task

Inability to access confined spaces

Personal event

Death of a family member

Marital difficulties

Change in health of a family member

Change in work responsibilities/assignment

Change in living conditions

Workplace distractions/interruptions during task performance

Confusion or disorientation about where one is in a task

Missed steps in a multi-step task

Not completing a task

Working environment is too dynamic

Memory lapse

Forgot

Other

Absenteeism

Vacations

Medical leave

Risk-taking behavior

(g) Environment / Facilities

The working environment/facilities can contribute to error. For example, temperature extremes (either too hot or too cold), high noise levels, inadequate lighting (reflection/glare, etc.), unusual vibrations, and dirty work surfaces could all potentially lead to maintenance errors. Concerns about health and safety issues could also contribute to maintenance technician errors.

Environment / Facilities examples to look for:

High noise levels

High noise impacts the communication necessary to perform a task

Extended exposure to noise reduces ability to concentrate and makes one tired

Noise covers up system feedback during a test

Hot

Work area is too hot so the task is carried out quickly

Extremely high temperatures cause fatigue

Long exposure to direct sunlight

Exterior components or structure too hot for maintenance technicians to physically handle or work on

Cold

Work area is too cold so the task is carried out quickly

Long exposure to low temperature decreases sense of touch and smell

Humidity

High humidity creates moisture on aircraft, part and tool surfaces

Humidity contributes to fatigue

Rain

Causes obscured visibility

Causes slippery or unsafe conditions

Snow

Causes obscured visibility

Causes slippery or unsafe conditions

Protective gear makes grasping, movement difficult

Lighting

Insufficient for reading instructions, placards, etc.

Insufficient for visual inspections

Insufficient for general maintenance activity

Excessive - creates glare, reflection, or eye spotting

Wind

Interferes with ability to hear and communicate

Moves stands and other equipment (creates instability)

Blows debris into eyes, ears, nose or throat

Makes using written material difficult

Vibrations

Use of power tools fatigues hands and arms

Makes standing on surfaces difficult

Makes instrument reading difficult

Cleanliness

Loss of footing/grip due to dirt, grease or fluids on parts/surfaces

Clutter reduces available/usable work space

Inhibits ability to perform visual inspection tasks

Hazardous/toxic substances

Reduces sensory acuity (e.g. smell, vision)

Exposure causes headaches, nausea, dizziness

Exposure causes burning, itching, general pain

Personal protective equipment limits motion or reach

Exposure causes general or sudden fatigue

Exposure causes general concern about long term effect on health

Power sources

Not labeled with caution or warning

Guarding devices missing or damaged

Power left on inappropriately

Circuit protection devices not utilized or damaged

Cords chafed, split, or frayed

Inadequate ventilation

Strong odor present

Burning or itching eyes

Shortness of breath

Sudden fatigue

Other

Area(s) not organized efficiently (difficult to find parts, work cards, etc.)

Area too crowded with maintenance technicians and/or other personnel

(h) Organizational Factors

The organizational culture can have a great impact on maintenance error. Factors such as internal communication with support organizations, trust level between management and maintenance technicians, management goals and technician awareness and buy-in of those goals, union activities, and attitudes, morale, etc., all affect productivity and quality of work. The amount of ownership the technician has of his/her work environment and the ability to change/improve processes and systems is of key importance to technician morale and self esteem, which in turn, affects the quality of task performance. This section is also the section to use when violations occur as a result of not following work processes or procedures.

Organizational Factors examples to look for:

Quality of support from technical organizations

Inconsistent quality of support information

Late or missing support information

Poor or unrealistic maintenance plans

Lack of feedback on change requests

Reluctance to make technical decisions

Frequent changes in company procedures and maintenance programs

Company policies

Unfair or inconsistent application of company policies

Standard policies do not exist or are not emphasized

Standard error prevention strategies don't exist or are not applied

Inflexibility in considering special circumstances

Lack of ability to change or update policies

Not enough staff

Not enough trained personnel

Not enough trained personnel at the time

Corporate change/restructuring

Layoffs are occurring

Early retirement programs drain experience

Reorganizations, consolidations and transfers cause more people to be in new jobs

Demotions and pay cuts

Frequent management changes

Union action

Contract negotiations create distractions

Historical management/labor relations are not good

Positive or negative communication from union leadership

Strike, work slowdown, or other labor action creates a disruption

Work process/procedure.

If the work process or procedure is followed but does not bring about the desired result, then check this box. Reasons that this might occur include:

Standard operating procedures (SOPs) incorrect

General maintenance manuals outdated

Inadequate inspection allowed

Process/procedure does not obtain the desired outcome

Work process/procedure not followed.

This box would be used for a violation of work processes or procedures that should have been followed, but were not followed. If this occurs, check this box. Then determine whether not following this process or procedure is a work group normal practice (norm). If it is a norm, then check box 9 below.

Skipped operational check

Required protective equipment not used

Did not use ”parts removed” tag

Work process/procedure not documented

No procedure for radio check before towing operation

No inspection criteria

No procedure for proper use of safety equipment

Work group normal practice (norm).

If a technician has not followed a work process or procedure that he should have, it is very important to determine whether most other technicians do the same thing in this situation.

Documented procedure—most people in the same situation do not follow the process or procedure

Undocumented procedure—most people do the procedure like the technician did.

Other

Company is acquired by another company

Work previously accomplished in-house is contracted out

Overall inadequate staffing levels

(i) Leadership / Supervision

Even though supervisors normally do not perform the tasks, they can still contribute to maintenance error by poor planning, prioritizing, and organizing of job tasks. Delegation of tasks is a very important supervisory skill and if not done properly, can result in poor work quality. Also, there is a direct link between the management/supervisory attitudes and expectations of the maintenance technician and the quality of the work that is performed.

Supervisors and higher-level management must also provide leadership. That is, they should have a vision of where the maintenance function should be headed and how it will get there. In addition, leadership is exhibited by management "walking the talk", that is, showing the same type of behavior expected of others.

Leadership / Supervision examples to look for:

Planning/organization of tasks

Excessive downtime between tasks

Not enough time between tasks

Paperwork is disorganized

Tasks are not in a logical sequence

Prioritization of work

Technicians not told which tasks to carry out first

Important or safety related tasks are scheduled last

Fault isolation is not performed with the most likely causes checked first

Delegation/assignment of tasks

Assigning the wrong person to carry out a task

Inconsistency or lack of processes for delegating tasks

Giving the same task to the same person consistently

Wide variance in workload among maintenance technicians or departments

Unrealistic attitude / expectations

Frequent dissatisfaction, anger, and arguments between a supervisor and a technician about how to do a task or how quickly a task should be finished

Pressure on maintenance technicians to finish tasks sooner than possible or reasonable

Berating individuals, especially in front of others

Zero tolerance for errors

No overall performance expectations of maintenance staff based on management vision

Amount of supervision

"Look over the shoulder" management style

Frequent questioning of decisions made

Failure to involve employees in decision-making

Other

Meetings do not have purpose or agendas

Supervisor does not have confidence in group's abilities

Management doesn't "walk the talk" and thereby sets poor work standards for maintenance staff

(j) Communication

Communication refers to the transfer of information (written, verbal, or non-verbal) within the maintenance organization. A breakdown in communication can prevent a maintenance technician from getting the correct information in a timely manner regarding a maintenance task.

Communication examples to look for:

Between departments

Written communication incomplete or vague

Information not routed to the correct groups

Department responsibilities not clearly defined or communicated

Personality conflicts create barriers to communication between departments

Information not provided at all or not in time to use

Between mechanics

Failure to communicate important information

Misinterpretation of words, intent or tone of voice

Language barriers

Use of slang or unfamiliar terms

Use of unfamiliar acronyms

Failure to question actions when necessary

Failure to offer ideas or process improvement proposals

Personality differences

Between shifts

Work turnover not accomplished or done poorly or quickly

Inadequate record of work accomplished

Processes not documented for all shifts to use

Job boards or check-off lists not kept up to date

Between maintenance crew and lead

Lead fails to communicate important information to crew

Poor verbal turnover or job assignment at the beginning of a shift

Unclear roles and responsibilities

Lead does not provide feedback to crew on performance

Crew fails to report problems and opportunities for improvement to lead person

Communication tools (written, phones, radios, etc.) not used

Between lead and management

Little or no communication exists

Goals and plans not discussed regularly

No feedback from management to lead on performance

Lead does not report problems and opportunities for improvement to management

Management fails to communicate important information to lead

Between flight crew and maintenance

Late notification of defect

ACARS/data downlink not used

MEL/DDG interpretation problem

Logbook write-up vague or unclear

Other

Computer or network malfunctions lead to loss of information

E-mail not used or ignored

(k) Other Contributing Factors

This section was put into the Users Guide in case a MEDA investigator found a contributing factor that did not fit into one of the ten contributing factors categories.

Since the field test, we have never seen the “Other” category used, but we have left it on the form just in case there may be a need some day.